## Slide 1: Digital Signal Processing
Maribeth Gandy

## Slide 2: What is DSP?
Signal Processing. One or more inputs come in, the processor modifies them in some way and produces one or more outputs
Techniques similar for Analog and Digital Processing
  Analog, precision, drift, noise, and distortion are problems
  Analog, delay is difficult
  Analog, hard to reconfigure dynamically, generality difficult
  However, for some applications digital is more complicated. Example, filtering a 3 MHz signal

## Slide 3: Why Digital is Preferred
Digital often means RAM and a generic processor, which is very powerful
  Digital pros as compared to Analog
    Programmable
    Dynamic range, low distortion, filter tuning, delays,random signal access, reconfiguration,presets,chainability, hardware design cost is low
  Analog pros as compared to Digital
    Frequency range, low power consumption, no software design cost
Notes: A digital filter is programmable, i.e. its operation is determined by a program stored in the processor's memory. This means the digital filter can easily be changed without affecting the circuitry (hardware). An analog filter can only be changed by redesigning the filter circuit.
Digital filters are easily designed, tested and implemented on a general-purpose computer or workstation.
The characteristics of analog filter circuits (particularly those containing active components) are subject to drift and are dependent on temperature. Digital filters do not suffer from these problems, and so are extremely stable with respect both to time and temperature.
Unlike their analog counterparts, digital filters can handle low frequency signals accurately. As the speed of DSP technology continues to increase, digital filters are being applied to high frequency signals in the RF (radio frequency) domain, which in the past was the exclusive preserve of analog technology.
Digital filters are very much more versatile in their ability to process signals in a variety of ways; this includes the ability of some types of digital filter to adapt to changes in the characteristics of the signal.

## Slide 4: What is DSP?
When talking about audio processing there are three main types
  Filtering. Processor alters the amplitude and possibly phase of a signal versus frequency
    Low Pass, High Pass, BandPass etc.
      Lots of equipment functions as filters
        speakers, amplifiers, mixers
  Delay
      Long delay results in echo, flanging if delay is short, reverb if delayed versions are filtered. Filtering also occurs due to cancellation and reinforcement
  Nonlinear changes
      Distortion, modulation, introducing new frequencies to signal
These can be used in various combinations

## Slide 5: Basics of a Digital Filter
Signal starts out as analog, V= x(t);
Signal is sampled at some interval (p), result are values taken from T = 0,p,2p,3p etc. x(np)
  List of samples x0,x1,x2,x3,x4…xn
The filter output values are calculated from this list of samples
  List of output samples y0,y1…yn
Notes: Input to the filter is x, Output from the filter is y

## Slide 6: Simple Filters
Unity Gain, y(n) = x(n), no effect
Simple Gain, y(n) = K * x(n), amplify, attenuate, or invert
Pure Delay, y(n) = x(n-1), delayed by sampling interval
Two-Term Difference, y(n)= x(n) – x(n-1)
Two-Term Average, y(n) = (x(n) + x(n-1)) /2
  Simplistic low pass, smoothing
  Can average with any number of terms
In the discrete domain it is easy to create “filters”

## Slide 7: Simple Filters
The “order” of a filter is the number of previous inputs required
  Zero Order,
    y(n) = 2x(n)
  First Order,
    y(n) = x(n-1)
    y(n) = 2x(n)+x(n-1)
  Second Order,
    y(n) = x(n-1) - x(n-2)
Notes: Y(n) = x(n-5), fifth order

## Slide 8: Simple Filters
Linear Time Invariant(LTI) systems
  No new frequencies are added to signal
  Test for linearity
    Superposition
      The response to a sum of the signals is the same as the sum of the responses to the individual signals,
        X1(n) + X2(n) results in Y1(n) + Y2(n)
    Homogeneity
      Amplitude of output is proportional to input so multiplying input by k would multiply output by k, kx(n) = ky(n)
  Test for Time Invariance
    The system behaves the same all the time. Delaying input by k will result in an output delayed by k
Causal, does not rely on future inputs
Notes: Superposition means linearity

## Slide 9: Simple Filters
Impulse Response
  Describes the behavior of an LTI system
  When an impulse response is input, output is impulse response. H(n)
    Can characterize all filters, used to determine how rooms effect sounds
  Since discrete signals are just a collection of impulses you can filter them by multiplying each sample by each value of the impulse response and then adding these scaled impulses together
    This is called convolution

## Slide 10: Convolution
The output of an LTI is the convolution of the input with the impulse response, y(n)=h(n) * x(n)
  Convolution is in the time domain
    To convolve, reverse the impulse response and slide it over x(n)
  The equivalent in the frequency domain is multiplication
    Faster and easier for hardware
      FFT made possible
www.jhu.edu/~signals/discreteconv
https://maxwell.ict.griffith.edu.au/spl/Excalibar/Jtg/Conv.html
Notes: Show example
Y0 = x0h0
Y1 = x0h1 + x1h0
Y2 = x0h2 + x1h1 + x2h0
Etc.
multiplication in frequency domain
www.jhu.edu/~signals/discreteconv

## Slide 11: Filter Coefficients
First Order
  Y(n) = a0 x(n) + a1 x(n-1)
Second Order
  Y(n) = a0 x(n) + a1 x(n-1) + a2 x(n-2)
Can be continued for any order
Coefficients are a0,a1,a2….They determine the characteristics of a filter

## Slide 12: FIR and IIR filters
We have been looking at non-recursive filters
  Output comes only from current and previous input values
Recursive filters also exist
  Output comes from input values and previous output values
These non-recursive filters are called finite impulse response (FIR)
  The impulse response is finite
The recursive filters are called Infinite Impulse Response (IIR)
  The impulse response is theoretically infinite because the previous outputs keep feeding into it, although they usually converge close to zero pretty quickly

## Slide 13: FIR and IIR filters
Surprisingly, IIR filters are more efficient
  Y(n) = x(n) + Y(n-1)
  This is expressed with two terms, whereas the FIR version would involve many additions and would require more storage
  Beware of positive feedback!
    Y(n) = X(n) + 2 * Y(n-1)
Notes:     Y(8) = x(8) + x(7) +x(6) + x(5) + x(4) + x(3) + x(2) + x(1) + x(0)
    Y(n) = X(n) + 2*Y(n-1)
      This would get loud very quickly

## Slide 14: IIR filters
So, what is the “order” of an IIR filter?
  Either the number of previous inputs or outputs required, depending on which is largest
    All IIR filters are at least 1st order
    Y(n) = x(n) + y(n-1) + y(n-2)
      2nd order
    In reality IIR filters usually use the same number of previous outputs and inputs
      Y(n) = x(n) + 3x(n-1) – x(n-2) + y(n) + y(n-1) – y(n-2)

## Slide 15: Coefficients of IIR filters
Similar to FIR but with the addition of the previous outputs
  Y(n) = (a0 x(n) + a1 x(n-1) - b1 y(n-1)) / b0
    Why the –b1? And what is b0?
    b0 y(n) + b1 y(n-1) = a0 x(n) + a1 x (n-1)
  Y(n) = x(n-1) – 2x(n-2) + y(n-1) – 3 y(n-2)
    Coefficients are b0 =1, b1 = -1, b2 = 3 a0 = 0, a1 = 1, a2 = -2
  5y(n) – 0y(n-1) - 6y(n-2) = 3x(n) + x(n-1)
    B0=5 b1=0 b2=-6 a0=3 a1 = 1 a2=0
Notes:       This is done so the equation can be rewritten as
        b0 y(n) + b1 y(n-1) = a0 x(n) + a1 x (n-1)
Y(n) = sum of a[k]*x[n-k] + sum of b[j]*y[n-j]
Y(n) = (x(n-1) +3x(n) + 6 y(n-2))/5
5y(n) – 0y(n-1) - 6y(n-2) = 3x(n) + x(n-1)
B0=5 b1=0 b2=-6 a0=3 a1 = 1 a2=0

## Slide 16: The Z transform
Used to generate freq domain representation of discrete signal
  …like Laplace for continuous signals
Complex number, real and imaginary component
Unit Delay operator
  Z-1
    Introduces a delay of one sample
      Z-1 x(n) = x(n-1)
      Z-1 (Z-1 x(n)) = x(n-2)
      Z-2 x(n) = x(n-2)

## Slide 17: Transfer Function
Describes a filter, allows us to determine its characteristics
  Substitute z transform into the previous equation for an IIR filter
    (b0 + b1z-1 + b2z-2)y(n) = (a0 + a1z-1 + a2z-2)x(n)
    Now we can calculate the transfer function which is the relationship of x(n) to y(n)
      Y(n)/x(n) = (a0 +a1z-1 + a2z-2)/(b0 +b1z-1 + b2z-2)

## Slide 18: Filter Coefficients
Why are the coefficients meaningful?
  They totally describe the filter…all FIR,IIR filters have the same form, all that differs is their coefficients
  Therefore to make a filter to your specifications you can use classic windowing equations (Hamming, Butterworth, Chebychev) to calculate what your coefficient values should be and then you are ready to process your signal
  Result will not be “ideal”.The parameters and windows you choose will determine the transition bandwidth (the sharpness of the dropoff) and the signal attenuation.
  Order will improve quality, but will cost more in terms of calculation and storage
  https://ccrma.stanford.edu/~jos/filters/http://www.falstad.com/dfilter/
Notes: ideal filter = infinite number of coefficients
Different windows will result in different tradeoffs
STANDARD FIR DEMO

## Slide 19: Filter Coefficients
Running white noise through filter and looking at spectrum is quick way of seeing the magnitude of the filter’s frequency response

## Slide 20: IIR Filter Design
Complex Numbers
  Contain a real part + an imaginary part
    Z = x + iy , (z = 3 + 6i)
      i being the square root of –1
    Represents the 2 dimensional aspects of a number, a vector.
  A waveform can be expressed in polar form (magnitude and phase, r and theta)
    This can also be represented as a complex number
      R =1, and theta = 45 degrees, same as .707 + .707i
      Theta = 90 degrees, 0 + i
      R = 2, 1.4 + 1.4i
    Multiplication of complex numbers
      Multiplying by imaginary number causes phase shift, by real causes magnitude shift,
Notes: Plot in polar form
(3 + 5i)(6 + 2i)
8 + 36i

## Slide 21: Poles and Zeros
Method for designing IIR filters
  Z plane, coordinates system from 0 – 2pi (0 – sampling frequency)
    Axis are real and imaginary (x,y)
    So only interested in 0 to pi every frequency greater would be aliased
    So, if sampling frequency was 44KHz , pi would be 22KHz, pi/2 would be 11KHz etc.

## Slide 22: Poles and Zeros
Poles and Zeros can be places in the Z plane
  Poles must be inside unit circle
  Zeros can be anywhere
  Must be placed in conjugate pairs when not on the real axis. (flipped around the real axis)
    .7 + .3j would require another zero at .7 - .3j
  Poles amplify signals, Zeros attenuate them
    So the closer a frequency is to a pole,the more it will be amplified. Opposite is true for zeros
  http://www.nst.ing.tu-bs.de/schaukasten/polezero/en_idx.html

## Slide 23: Poles and Zeros
Place poles and zeros to design a filter
  For example, a simple bandpass filter could consist of a pair of conjugate poles, the frequency that is effected by the pole is the one at the same angle as the pole
  Filter coefficients can then be calculated from the standard H(z) transfer function

## Slide 24: Poles and Zeros
Place poles and zeros to design a filter
  The magnitude of the pole determines the pass band width and the magnitude.
    The closer the pole is to the radius of 1 the narrower the pass band and the greater the amplification
    Conjugate also has effect

## Slide 25: Poles and Zeros
a0 (z-z1) (z-z2) (z-z3) (z-z4) ...
H(z) = --------------------------------------
(z-p1) (z-p2) (z-p3) (z-p4) ...
Z is the frequency in complex form, Ps are the positions of the poles and #Zs are the positions of the zeros in complex form. A0 is the first input coefficient.

## Slide 26: Poles and Zeros
For our bandpass filter this simplifies to
  H(z) = a0 / (z-p1)(z-p2), since we only have two poles and no zeros
  For your Ps substitute in the positions
    p1 = (px, py) = px + ipy, p2 = (px,-py) = px - ipy
  Result is z0 = -(-2px)z (-1) - (px2 + py2)z(-2)
  And now we have arrived at the z transform version, so we can look at the equation as
    output(t+0) = a0 input(t) -(-2px)output(t-1) - (px2 + py2)output(t-2)
    So we can determine our coefficients
    We can also calculate the different parameter formulas

## Slide 27: Poles and Zeros
Working through the substitutions will yield
SR = sampling frequency
f = passband center frequency
r = [0,1)
phx = cos(2pi f/SR), phy = sin(2pi f/SR)
a0 = (1-r) * sqrt(r*(r-4*phx+2)+1)
b1 = 2*r*phx
b2 = -r2
output(t) = a0 * input(t) + b1 * output(t-1) + b2 * output(t-2)
For more information
  http://yehar.com/blog/?p=121

## Slide 28: Poles and Zeros
Adding a zero between the conjugate poles would reduce the effect of the conjugate pole
  If we don’t use conjugate poles the coefficients are complex numbers and the resulting signal is complex
A filter with only zeros is an FIR filter.
Phase response is also a factor in filter design
Filter design is an art
  Calculating filter coefficients from the desired frequency response is still open problem
Notes: IIR filter DEMO

## Slide 29: Transforms
A transform is a mathematical tool used to move between the time and frequency domains.
Convolution in the time domain equals multiplication in the frequency domain
  Convolution although easy conceptually is computationally intensive
  Therefore it is often preferable to transform into the frequency domain, multiply and then transform back
  It is also useful to transform a signal or filter in order to understand its spectral characteristics

## Slide 30: Fourier Transform
Is intended for generating a continuous spectrum from a continuous infinite signal.
Therefore, for your digital audio purposes we use the Discrete Fourier Transform (DFT) which converts a discrete signal into a discrete spectrum

## Slide 31: Fourier Transform
DFT is computationally intensive, so the Fast Fourier Transform(FFT) is used
  O(N2) vs. O(N(log(N))
  FFT takes advantage of redundancy and symmetry
    Just an efficient method of doing DFT
    Decomposes data into sets then those sets are broken into smaller sets (e.g. 32 -> 2 sets of 16 -> 4 sets of 8 etc.)
    Usually requires that the number of inputs is an integral power of 2
    Result is the real and imaginary parts of the signal or filter (magnitude and phase)

## Slide 32: Fourier Transform
Theoretically, we can move back and forth between the time and frequency domain without losing any information
  In practice this is not true
  But we use the two domains because some signals are easier to visualize or contain less information in one of the domains
    For example, a sin wave consists of a lot of data in the time domain but just freq, magnitude and phase in the frequency domain

## Slide 33: Fourier Transform
The FFT assumes your signal is periodic and infinite
  There is no concept of time
  But your sampled data is finite
When you feed in a signal to the FFT it will assume that that signal is periodic for all time
  The result is correct if the signal segment is periodic and is appropriately sized so that an integral number of periods fit into the window.
  However, this will not often happen and spectral leakage occurs
    The frequency spectrum of that signal is broadened
    This effects the frequency resolution. The amount of space required between two frequencies for them to be seen as distinct
Notes: Draw picture of how the FFT sees your finite signal
Show how it can work…and show glitches…which introduces wrong frequencies

## Slide 34: Fourier Transform
The way to lessen these leakage effects are to use “windowing”
  Windowing means the ends of the signal are shaped so that they match
    Best way to do this is to make the value and the derivatives at the ends of the signal 0. Then they will always match up nicely
Notes: Draw effect of window

## Slide 35: Fourier Transform
However, windowing is distorting the signal
Frequencies are distorted and signal attenuated

## Slide 36: Fourier Transform
There are many windowing functions to choose from that allow a tradeoff in frequency resolution versus distortion and increase in signal to noise ratio
Notes: WINDOW DEMO

## Slide 37: Fast Fourier Transform
Practical considerations
  Number of points to take an FFT on
    Smaller allows you to capture the frequency changes with time, but will make it impossible to detect lower frequencies
    Larger allows you to detect those low frequencies but the changes will be lost

## Slide 38: Fast Fourier Transform
Practical considerations
  Bins
    The DFT (and thus the FFT) have a finite frequency resolution. You have a finite number of frequencies you can resolve or bins you can fill. Each bin will have the energy for the frequencies in the signal that are covered by that bin
http://web.mit.edu/newsoffice/2012/faster-fourier-transforms-0118.html

## Slide 39: References
Digital Audio Processing, Doug Coulter
Principles of Digital Audio, Ken Pohlmann
Discrete-Time Signal Processing, Oppenheim, Schafer
Notes: Digital Audio Processing
Digital Signal Processing
http://www.dsptutor.freeuk.com/
http://www.student.oulu.fi/~oniemita/DSP/DSPSTUFF.TXT
Demos
http://www.bores.com/courses