## Slide 1: Digital Audio
Maribeth Gandy
Notes: Principles of Dig Audio, Pohlmann
http://www.tc.umn.edu/~erick205/Papers/paper.html
http://www.earlevel.com/Digital%20Audio/index.html

## Slide 2: Analog to Digital Conversion
Analog = Continuous
Digital = Discrete
Analog becomes Digital via sampling
Is information lost? No
  A continuous signal can be reproduced from discrete samples
    An analogy is a movie where our brain fills in missing information. With digital signals the missing information comes from interpolation
http://www.earlevel.com/main/category/digital-audio/

## Slide 3: Sampling Frequency
How fast should we take samples?
  Sampling theorem
    A continuous band-limited signal can be replaced by a discrete sequence of samples without any loss of information.
    the sampling frequency must be greater than or equal to twice the highest frequency in the original analog signal
    Nyquist frequency, FS < 2F
      Aliasing
        Wagon wheel effect http://www.youtube.com/watch?v=YpMtanpsVeE http://www.youtube.com/watch?v=gzSYnGEqof8
Notes: http://www2.egr.uh.edu/~glover/applets/Sampling/Sampling.html

## Slide 4: Sampling Frequency
When aliasing occurs the result is folding
  FA = | F – ((K + 1)FS)/2| where K*FS/2<=F<=(K+2)FS/2, K is odd integer that satisfies the inequality
  the audible frequency is half the sampling frequency minus the amount the frequency exceeded half the sampling frequency
    44 KHz , 27KHZ is sampled, resulting audio is 17 KHz
    http://www.cems.uvm.edu/~mirchand/classes/EE171/Mitra/media/demos/demos.htm
Notes: K is for where F is much larger than Fs, F of 70, Fs of 44, K = 3 to satisfy inequality
http://www.cems.uvm.edu/~mirchand/classes/EE171/Mitra/media/demos/demos.htm#D1

## Slide 5: Sampling Frequency
Higher sampling freq will not improve reconstruction of freq within the FS/2 range.
  Higher sampling freq requires faster circuitry, more storage space, CD->DVD Audio->Super Audio CD
  Supposedly, human hearing range stops around 20KHz

## Slide 6: Sampling Frequency
Steps in Analog to Digital(ADC) and Digital to Analog Conversion(DAC)
  To avoid aliasing, filter signal before sampling
    “Brickwall” Low Pass Filter, Filter not perfect so “guard band” is used
    Sample input waveform
      Result in frequency domain contains images of the original spectrum centered at multiples of the sampling frequency
    Another Low Pass Filter with the same characteristics as the first. “ reconstruction filter”
    http://www2.egr.uh.edu/~glover/applets/Sampling/Sampling.html
    http://www.jhu.edu/~signals/sampling/index.html
Aliasing must be prevented, because once it has happened it can’t be undone
Notes: http://www.nt.e-technik.uni-erlangen.de/~rabe/SYSTOOL/SYSTOOL2.02/HTTP/sampl.htm
Diagrams from Pohlmann book

## Slide 7: Quantization
A sample will represent the amplitude of the signal at that point in time
  The analog value of the amplitude will be converted to a discrete value
    Quantization
    Sampling = Time, Quantization = Value, together they characterize an acoustic event
  Therefore the bit resolution is very important
    Finite word length means measuring error introduced
    Sampling is lossless, but quantization is not
    16 bit = 65,536 different levels, 2^n is number of levels
    Error will not exceed ½ of the interval
Notes: The measuring error can not be avoided
Speech can barely be intelligible with 1 bit
So adding a bit doubles the number of levels
24 bit accuracy of distance between NY and LA…accurate to 9 inches

## Slide 8: Quantization
Signal-to-error ratio
  S/E(dB) = 6.02n + 1.76, where n is number is the number of bits
    16 bits = 98 dB, 15 bits = 92 dB
      An additional bit will increase the ratio by 6 dB
Distortion introduced to signal
  As the signal level decreases the percentage of distortion increases
    16 bit, but half amplitude signal, value never exceeds 32,768. Therefore , it is quantized with 15 bit resolution
  Heard as white noise in high amplitude broadband signals
  For low amplitude or narrow bandwidth signals distortion is more evident
    Aliasing can occur, because the distortion creates freq components above the Nyquist frequency
  How the quantization values are assigned is also important
    MP3 coding not linear
Notes: As statistical correlation increases the noise becomes less benign…in high band, the successive values are random…this is not true for low amp or narrow bandwidth.
Although linear is normally used..this changed with perceptual coding like MP3

## Slide 9: Sampling and Quantization
Mozart versus ABBA
44, 16
44, 16
44, 8
44, 8
22, 16
22, 16
11, 16
11, 16
11, 8
8, 16
8, 8
22, 8
22, 8
8, 16
8, 8
2, 16
2, 8
2, 8
Notes: 44-16
44-8
22-16
22-8
11-16
11-8
8-16
8-8
2-16
2-8

## Slide 10: Dithering
Could add more bits to reduce error, but low level signal will always have distortion
Dithering is a more efficient technique
  Dithering is adding low level white noise to the signal
    Finger example
    Lets us hear components below the level of our least-significant bit
    WWII bombers vibrating the mechanical computer
  De-correlates noise from input signal
    Tradeoff of hiss for distortion
  Various dither functions used
    Rectangle, triangular, Gaussian
Less bits = more dithering required
Notes: Remember random error is white noise which is okay
finger examples
Example is waveform with eamplitude of 1 quantization interval, square wave results
Example of WWII bombers with mechanical computer that worked better when flying because of vibrations…first example of dithering..they put vibrating motors into machines

## Slide 11: Dithering
http://www.earlevel.com/main/2010/11/07/the-sound-of-dither/
Notes: Remember random error is white noise which is okay
finger examples
Example is waveform with eamplitude of 1 quantization interval, square wave results
Example of WWII bombers with mechanical computer that worked better when flying because of vibrations…first example of dithering..they put vibrating motors into machines

## Slide 12: Phase Distortion
Phase distortion can occur from sources such as analog equalization and DAC filters
  Error is constant and effects a group of frequencies
Humans can’t hear relative phase shift of static waveform
Human’s can hear phase shift in dynamic waveforms, transients
Voice with phaser effect
Notes: Of course you can hear phase shifting done on purpose, done for effects
Depends on music, the frequencies, amount of phase error
http://en.wikipedia.org/wiki/Phaser_(effect)

## Slide 13: Oversampling
Oversampling is exceeding the Nyquist frequency
  Can relax demands such as “brickwall” filter
  Signal to Noise ratio is boosted
  Quantization noise is reduced in audible band
  Same as increasing bit depth
When used during analog to digital conversion, data is sampled at high frequency and then decimated.
Notes: Draw graph of oversampling

## Slide 14: Oversampling
When used in DAC
  Not sampling at higher rate
  Samples are introduced between samples and set to zero. Then their values are created via interpolation.
    Moves the location of the “folding” point FS/2 so you can use a LPF with a gradual slope
    Quantization noise is now spread over wider band and power density is reduced
  Noise Shaper is applied (combined with dithering)
    Alters the frequency spectrum of the error signals so as to move most of the quantization error out of the audible frequency range
    Shapes the quantization noise instead of leaving it as white noise
Notes: One problem with this is that, ideally, we want to block everything above the Nyquist rate (22.05 KHz), but let everything below it pass unaffected. Filters aren't perfect, though. They have a finite slope as they begin attenuating frequencies, so we have to compromise. If we can't keep 22 KHz while blocking everything above it, we'd certainly like to shoot for 20 KHz. That means the low-pass filter's cutoff must go from about 0 dB attenuation at 20 KHz to something like 90 dB at 22 KHz—a very steep slope.
While we can do this in an analog filter, it's not easy. Filter components must be very precise. Even so, a filter this steep has a great deal of phase shift as it nears the cut-off point. Besides the expense of the filter, many people agree that the phase distortion of the upper audio frequencies is not a good thing.
Now, what if we had sampled at a higher rate to begin with? That would let us get away with a cheaper and more gentle output filter. Why? Since the reflections are wrapped at the sampling frequency and its multiples, moving the sampling frequency that far up moves the reflected image far from the audio portion we want to preserve. We don't need to record higher frequencies—the low-pass filter will get rid of them anyway—but simply having more samples of our audio signal would be a big help.
This is where interpolation comes in. We calculate what it would look like if we had sampled with more points to begin with. If we could have, for instance, eight times as many sample points running at eight times the rate ("8X oversampling"), we could use a very gentle filter, because instead of 2 KHz of room to get the job done, we'd have 158 KHz.
In practice, we do exactly this, following it with a phase linear digital "FIR" (finite-impulse response) filter, and a gentle and simple (and cheap) analog low-pass filter.

## Slide 15: Digital to Analog Conversion
Ideal DAC impulses passed through reconstruction filter
Notes: Example of cycling the light in a room to get intermediate values
1 bit at 11 MHz
Puts quantization noise out of the audible band.

## Slide 16: Digital to Analog Conversion
1bit ADC/DAC with oversampling is superior
  Sampling with smaller word size, but at much higher frequency
    Low cost (1 bit DAC common in consumer electronics)
    Distortions and non-linearities reduced
      Quantization noise now out of the audible band
      Phase distortion reduced
  http://repository.upenn.edu/cgi/viewcontent.cgi?article=1144&context=ese_papers
DACs important because they are at the beginning of the chain
  Total Harmonic Distortion THD
  Dynamic Range
High end systems may have external DAC
Notes: Example of cycling the light in a room to get intermediate values
1 bit at 11 MHz
Puts quantization noise out of the audible band.

## Slide 17: Jitter
Jitter is a time instability during sampling or playback
Anti-jitter circuits, buffering, and jitter correction in software
  Timebase correction (analog recordings on mechanical media)
  products sold to reduce jitter and other errors

## Slide 18: Why digital is better
Why do we choose digital over analog?
  Ideally analog should be better, no information is lost.

## Slide 19: Why digital is better
Digital circuits are complex, but precision not needed for digital (1 or 0)
Performance can be improved simply by increasing word size or sample rate. Cheaper
Less maintenance. Analog circuits change over time
Digital information is more durable. Easier to correct errors (in media, from transmission etc.)
Can create new sounds purely from numbers, and can control them precisely.
Every analog copy introduces more noise

## Slide 20: Why digital is better
With analog media, oftentimes the mechanism has to touch the media
With analog system the total noise is the summation of all distortion and noise from each component in signal path.
Analog equipment often have uneven frequency response, lower dynamic range.

## Slide 21: Error Correction
With analog audio there is no way to do error correction
With digital error detection and correction is both possible and necessary.
  Data can be encoded or redundant
  Upon detection the error can be corrected, or concealed
  Necessary due to defects in media and harsh environments
  CD and DVD systems approach the computer industry standard of an error rate of 1 uncorrectable error in 1 trillion bits

## Slide 22: Sources of Errors
Error correction mainly focused on stored and transmitted data
  Media can become damaged or can contain defects
  Transmission can become corrupted do to many types of interference
    Noise, attenuation, limited bandwidth, reflection, ringing
Types of errors
  Random-bit errors
    Occur singly, easy to correct
  Burst error
    Large error that may effect many bits
    One property of a correction system is therefore, burst length, or how many erroneous bits in a row can be corrected.
    That is why a scratch in a CD perpendicular to the track is easier to correct than one along a track

## Slide 23: Error Correction
There will always be errors, therefore redundancy is necessary
But redundancy must be minimized to reduce data size
The steps in an error-correction system
  Error detection, check the data for validity
  Error correction replaces error with new valid data
  If error can’t be fixed, conceal with approximately correct data
  If all else fails mute the signal for severely erroneous data

## Slide 24: Error Detection
Just having multiple copies of data is not enough. Which copy do you believe?
Single- bit parity
  Extra bit indicates whether there was an even or odd number of 1s in number
    Detects odd numbers of errors, okay for random-bit errors
Cyclic Redundancy Check Code (CRCC)
  Parity word formed
    Could be from sum of bits in data
    In reality uses more complex division of data and remainder is appended to data. Upon reception the data is divided to check for errors
      Some errors can then be corrected with this technique as well
Notes: 1011011010 = 6 0110

## Slide 25: Error Correction
Simplest solution is to detect error then go to redundant track for correction.
Redundant samples should be separated so as to reduce chance of it be corrupt too.
Channel Coding
  CD uses 20 bits to encode the 2^16 different values so as to avoid difficult to read sequences like 0000000100000000.
  Errors can also be detected with this method, and data can be changed to the closest allowed value.
Interleaving used on CDs
  Data stored non-sequentially around a circuit

## Slide 26: Error Correction
Many more sophisticated techniques are also used
  Block Codes
    Parity words from blocks of data
  Hamming Codes
    Can pinpoint location of error
  Convolution Codes

## Slide 27: Error Concealment
Errors may not be detected
  These can not be concealed
Errors may be detected but not corrected
  These can be concealed
    Interpolation
      Use surrounding data to generate new data
    Muting
      Silence is better than a click
        Sample is just set to zero
        May fade out and back in to conceal mute
Error concealment will cause errors in duplication

## Slide 28: References
Principles of Digital Audio: fourth edition, Ken Pohlmann,2000